Ahead V5000 version A & B.

  Allows up to four boards in one system.


  103h (R/W): Multiple Chip ID Register
  bit 0-3  Must match PowerUp register (3CEh index 1Fh bits 4-7).

  3C2h (W): Misc Output Register
    bit 5  Bit 0 of bank register.         (Ahead A)

  Note: This register can be read at 3CCh.


  3CEh index  Ch (R/W): mode
  bit 0-1  Misc control. 0=standard text mode, 1=enable
             8 simultaneous fonts  2&3 reserved.
        2  Reserved
        3  High speed sequencer enable
        4  16 bit memory access enable
        5  Enhanced mode enable
      6-7  Emulation mode. 0=VGA, 1=EGA, 2=Hercules and 3=CGA

  3CEh index  Dh (R/W): Segment            (Different for Ahead A and B)
  bit 0-2  (Ahead A) Bank No. bit 1-3
                     Bit 0 is in 3C2h bit 5.
      0-3  (Ahead B) Read Bank No.
      4-7  (Ahead B) Write Bank No.

  3CEh index  Eh (R/W): Clock
  bit 1-3  Reserved
      4-7  Divide input clock 0-3 by 2.

  3CEh index  Fh (R/W): Master Enable Register
  bit 0-3  Chip version number  (Read Only)
           0=Ahead A, 1=Ahead B
        5  Enable extended registers if set

  3CEh index 10h (R/W): Trap
    bit 0  Enable CRTC access
        1  Enable 6845 access
        2  Enable CRTC access to cause trap
        3  Enable 3B8h, 3BFh to cause trap
        4  Enable 3D8h, 3D9h to cause trap
        5  Enable 3Cxh to cause traps
        7  Select 6845 as CRT controller

  3CEh index 11h (R/W): Trap source
    bit 0  3Dxh
        1  3B5h, 3D5h
        2  3B8h, 3D8h
        3  3D9h
        4  3BFh
        5  3Cxh
      6-7  Reserved


  3CEh index 12h (R/W): Attribute
  bit 0-5  Reserved
        6  Lock VGA internal palette
        7  Enable CGA palette when in CGA mode

  3CEh index 13h (R/W): Diagnostics
  bit 0-7  Reserved

  3CEh index 14h (R/W): Lock
    bit 0  Lock Sync polarity in 3C2h bit 6,7.
        1  Lock CRTC horizontal timing
        2  Lock CRTC vertical timing
        3  Lock CRTC index 9        !Hmm.
        4  Lock CRTC index 9
        5  Lock CRTC index 0Ah, 0Bh
        6  Lock CRTC index 13h
        7  Lock Clock select in 3C2h bit 2,3.

  3CEh index 15h (R): 3B8/3D8 Readback
  bit 0-7  Mono/CGA register 3B8h/3D8h readback value

  3CEh index 16h (R): 3BF/3D9 Readback
  bit 0-5  CGA Register 3D9h readback
      6-7  Mono register 3BFh bit 0-1 Readback.

  3CEh index 17h (R/W): Miscellaneous
    bit 0  Must be 1
        1  Must be 0
      2-7  Reserved

  3CEh index 1Ch (R/W): CRTC Control
  bit 0-1  Bit 16-17 of CRTC start address
      2-3  0=normal, 3=Interlaced, 1&2 reserved.

  3CEh index 1Dh (R/W): Control
  bit 0-7  Reserved

  3CEh index 1Eh (R/W): Scratch
  bit 0-7  Used by BIOS for flags

  3CEh index 1Fh (R): PowerUp
  bit 0-1  Memory type. 0=2x44256 (256k), 1=4 or 16 x44256 (512K/2M),
                        2=8 or 16 x4464 (256K or 512K), 3=8x44256 (1M)
        2  0 for 24k BIOS, 1 for 32k BIOS.
        3  16 bit BIOS
      4-7  Multiple Chip ID
            0= ID 0  BIOS Enabled, 1=ID 1  BIOS Enabled
            2..15  ID 2..15  Bios Disabled.

 46E8h (R/W): Setup Control Register
    bit 3  0 for VGA disabled, 1 for enabled
        4  0 for Setup mode, 1 for normal mode.
      5-7  Reserved






  Bank switching:

  The Ahead A has one bank register with bit 0 in 3C2h bit 5 and
  bits 1-3 in 3CEh index 0Dh.

  The Ahead B has separate read and write banks in register 3CEh index Dh.


  Memory locations:

  $C000:$25  5 bytes  'AHEAD'



  ID Ahead chipset:

  portw[$3CE]:=$200f;
  case port[$3CF] of
    $20:Ahead A (with 512k ??)
    $21:Ahead B (with 1M ??)
  end;


  Modes:

  22h  T   132   44  16 (8x8)
  23h  T   132   25  16 (8x14)
  24h  T   132   28  16 (8x)
  25h  G   640  480  16 planar
  26h  G   640  480  16 planar
  2Fh  T   160   50  16
  34h  T    80   66  16
  50h  T   132   25   2
  52h  T   132   44   2
  60h  G   640  400 256 packed
  61h  G   640  480 256 packed
  62h  G   800  600 256 packed
  63h  G  1024  768 256 packed   (Ahead B only)
  6Ah  G   800  600  16 planar
  70h  G   720  396  16 planar
  71h  G   800  600  16 planar
  74h  G  1024  768  16 planar
  75h  G  1024  768   4
  76h  G  1024  768   2


  Note: Mode 75h has even bytes in planes 0&2, and odd bytes in planes 1&3.